## Slide 1: Hardware-Software Co-Design
Flexible Per-Row Sparsity Patterns
Sozos Koulas – Undergraduate Student
Ilias Papalambrou
Dimosthenis Masouros
Dιmιtrios Soundris
School of Electrical and Electronics Engineering at NTUA

## Slide 2: Introduction
The Evolution of Structured Sparsity in Deep Learning

## Slide 3: The Challenge of Modern AI
Exponential growth in model parameters
Increasing demand for real-time inference
Memory Bandwidth and Energy Constraints
Necessity for Advanced Compression Techniques

## Slide 4: Defining Matrix Sparsity
Unstructured
Structured
Semi-Structured
Maximum flexibility with zero weights anywhere
High Accuracy but extremely difficult to accelerate in Hardware
Entire Rows/Channels Removed
Easy for Hardware but often leads to significant accuracy degradation
Fine-grained patterns like 2:4
Bridges the gap between Accuracy and Hardware Efficiency

## Slide 5: Motivation
Why move beyond the static 2:4 Pattern?

## Slide 6: Current State: NVIDIA 2:4
50% Fixed Sparsity Ratio
High Hardware Throughput (2x Speedup)
Uniformity is a Limitation
Cannot Adapt to “Important” Rows

## Slide 7: Pruning Layers of Llama-3.2-1B
Notes: Από το διάγραμμα αυτό παρατηρούμε ότι με ελαφρύ pruning σε όλα τα layers η ακρίβεια του μοντέλου παραμένει υψηλή και κοντά στο Baseline. Με αύξηση του threshold παρατηρείται αισθητή πτώση της απόδοσης του μοντέλου.
Σημασία έχει να δούμε την ευαισθησία των Layers, όπου τα πρώτα layers με pruning έχουν καταστροφικά αποτελέσματα σε αντίθεση με τα τελευταία layers, τα οποία και με aggressive pruning παραμένουν με ψηλό accuracy.
Αυτό είναι λογικό καθώς τα πρώτα layers είναι πιο κοντά στην είσοδο με αποτέλεσμα να επικρατεί το φαινόμενο σπασμένου τηλεφώνου, ενώ τα layers που είναι κοντά στην έξοδο είναι πιο ανθεκτικά καθώς η πληροφορία έχει ήδη επεξεργαστεί αρκετά από τα προηγούμενα layers.

## Slide 8: The Need for Adaptation
One Size
Does Not Fit All
Theoretical Thesis
Different parts of a Neural Network possess different sensitivity to pruning
A static 50% ratio across all rows ignores the intrinsic hierarchical importance of weights
Our goal is to allow the hardware to handle variable sparsity while maintaining the acceleration benefits of the 2:4 structure

## Slide 9: Proposed Solution
Heterogenous Per-Row Sparsity

## Slide 10: Flexible Sparsity
Our architecture expands the 2:4 window concept to support multiple ratios (e.g. 2:4, 2:8, 2:16 and 2:32) dynamically per row or batch of input.
This allows “dense” row to keep more weights and “sparse” rows to keep less weights optimizing the accuracy-efficiency target

## Slide 11: Core Architectural Changes
Dynamic Multiplexing: Adaptive logic to route non-zero elements based on row/batch level metadata
Metadata Encoding: Extending the 2-bit index per 2:4 block to include row/batch level density flags
Run-time Sparsity Changes: Ability to change sparsity patterns on run-time per row-batch

## Slide 12: Baseline Architecture
Dense GEMV Module

## Slide 13: Top Dense Module

## Slide 14: C Core Dense Module

## Slide 15: C Block Dense Module

## Slide 16: Sparse Architecture
Sparse 2:N GEMV Module

## Slide 17: Top Sparse Module

## Slide 18: C Core Sparse Module

## Slide 19: C Block Sparse Module

## Slide 20: Results
Sparse 2:N GEMV vs Dense GEMV Module

## Slide 21
Chart: Speed-up vs dense across 11 GEMV shapes (300 MHz)
| G1 | G2 | G3 | G4 | G5 | G6 | G7 | G8 | G9 | G10 | G11 | GEOMEAN
2:4 | 2.0023 | 2.0307 | 1.9512 | 1.979 | 2.0023 | 2.0195 | 1.9978 | 1.9746 | 2.0206 | 2.0022 | 2.02 | 1.9999
2:8 | 3.8918 | 3.9712 | 3.8724 | 3.9334 | 4.0073 | 3.9889 | 3.9829 | 3.963 | 3.9729 | 3.9875 | 4.0168 | 3.9623
2:16 | 7.7542 | 7.8612 | 7.7715 | 7.8708 | 8.0742 | 7.9566 | 7.9751 | 8.0018 | 7.9963 | 7.9686 | 8.0263 | 7.9318
2:32 | 15.1937 | 15.7401 | 15.5015 | 15.4823 | 16.1916 | 15.7603 | 16.0367 | 15.8258 | 16.0056 | 15.9569 | 16.2632 | 15.8113

## Slide 22
Chart: ACTUAL THROUGHPUT ACROSS 11 GEMV SHAPES (300MHZ)
| 512x512 | 768x768 | 1024x1024 | 3072x768 | 768x3072 | 4096x1024 | 1024x4096 | 2048x2048 | 4096x4096 | 8192x2048 | 2048x8192
dense | 74.1 | 73.56 | 75.48 | 74.52 | 73.94 | 73.85 | 74.2 | 74.45 | 74.17 | 73.91 | 73.79
2:4 | 74.18 | 74.69 | 73.64 | 73.74 | 74.03 | 74.57 | 74.12 | 73.51 | 74.93 | 73.99 | 74.53
2:8 | 72.09 | 73.03 | 73.07 | 73.28 | 74.08 | 73.64 | 73.88 | 73.77 | 73.66 | 73.68 | 74.1
2:16 | 71.82 | 72.29 | 73.32 | 73.32 | 74.63 | 73.45 | 73.97 | 74.47 | 74.13 | 73.62 | 74.04
2:32 | 70.37 | 72.37 | 73.13 | 72.11 | 74.83 | 72.74 | 74.37 | 73.64 | 74.19 | 73.71 | 75.01

## Slide 23
Chart: A matrix with four different sparsities costs the sum of its parts
| Predicted | Measured
2:4 segment | 3571.4
2:8 segment | 1789.9
2:16 segment | 901.8
2:32 segment | 453.4
launch overhead | 700.7
Measured kernel span | 7417.217

## Slide 24
Chart: Latency per matrix across shapes and sparsities (300 MHz)
| 512x512 | 768x768 | 1024x1024 | 3072x768 | 768x3072 | 4096x1024 | 1024x4096 | 2048x2048 | 4096x4096 | 8192x2048 | 2048x8192
dense | 7.0757 | 16.036 | 27.7848 | 63.3179 | 63.8128 | 113.5937 | 113.0586 | 112.6688 | 452.4202 | 453.9778 | 454.7025
2:4 | 3.5338 | 7.8966 | 14.2399 | 31.9946 | 31.8702 | 56.2487 | 56.5902 | 57.058 | 223.9066 | 226.7357 | 225.1055
2:8 | 1.8181 | 4.0381 | 7.175 | 16.0976 | 15.9243 | 28.4773 | 28.3859 | 28.4299 | 113.8756 | 113.8514 | 113.2006
2:16 | 0.9125 | 2.0399 | 3.5752 | 8.0447 | 7.9033 | 14.2766 | 14.1765 | 14.0804 | 56.5787 | 56.9705 | 56.6514
2:32 | 0.4657 | 1.0188 | 1.7924 | 4.0897 | 3.9411 | 7.2076 | 7.05 | 7.1193 | 28.2664 | 28.4503 | 27.9589
MIXED | 1.6602 | 3.7231 | 6.4935 | 14.7399 | 14.71 | 26.3139 | 26.0928 | 26.2266 | 104.3351 | 106.1097 | 104.3028

## Slide 25
Chart: DSP occupancy during compute
| dense | 2:4 | 2:8 | 2:16 | 2:32 | MIXED
300 MHz | 0.9592 | 0.9699 | 0.9603 | 0.9567 | 0.955 | 0.9693
325 MHz | 0.9671 | 0.965 | 0.9562 | 0.9578 | 0.9453 | 0.9704

## Slide 26
Chart: Energy per row (board power)
| dense | 2:4 | 2:8 | 2:16 | 2:32
300 MHz | 887.5 | 508 | 253.7 | 128.4 | 65.1
325 MHz | 832.8 | 474.1 | 236 | 121.3 | 61.4

## Slide 27
Chart: Board power is flat across sparsity
| dense | 2:4 | 2:8 | 2:16 | 2:32
Board load (W) | 31.297 | 35.442 | 35.327 | 35.413 | 35.521

## Slide 28: Innovations
Sparse 2:N GEMV vs Dense GEMV Module

## Slide 29: Main Implementation Innovatios